## Slide 1: Video Anomaly Detection and Classification for Autonomous Deep-Space Robotics
Rohaan Ahmed
Mission Systems Engineer, MDA Space
PhD Computer Science (Student), LIA Lab, Ryerson University
15 December 2020

## Slide 2
Motivation & Problem Statement
Dataset and Data Engineering
Unsupervised Model
  Model Architecture
  Model Training & Evaluation Metric
  Model Testing
Supervised Classification
Results & Future Work
Content

## Slide 3: Motivation
The Space industry is seeing rapid growth, with a focus on colonizing the Moon, Mars, and beyond.
Robotic systems operating in deep space will require high levels of autonomy
  Autonomous Operation
  Maintenance
  Self repair
  Navigating unexpected situations
One such large program is the upcoming Lunar Gateway
Lunar Orbital Platform Gateway (LOP-G) (Courtesy: NASA)

## Slide 4: Canadarm3 and Lunar Gateway
Canadarm3 will be Canada’s contribution to the Lunar Gateway
Similar to Canadarm2, it will be used for:
  Construction
  Maintenance
  Inspection
  Capture of visiting spacecraft
  Module relocation
  Support of spacewalks.
Unlike Canadarm2, it will need to be fully autonomous
  Comm Delays and Dropouts
  Bandwidth Limitations
Canadarm3 Concept Image (Courtesy: CSA)
Canadarm2 on the International Space Station (Courtesy: CSA)

## Slide 5: Project Objective
Develop Proof of Concept AI-enabled Video Anomaly Detection and Classification system
  Input: In-space videos generated on-board
  Output: Video-clips classified as Anomalous or Non-Anomalous

## Slide 6: Dataset & Data Engineering
UCSD Anomaly Detection Dataset
Use UCSD Dataset as surrogate for difficult to obtain Space Datasets
UCSD Dataset is consists of 34 Train and 36 Test videos, 200-frames each.
Acquired with a stationary camera mounted at an elevation, overlooking pedestrian walkways with variable crowd densities.
Train Videos: “Normal” conditions only, ex. pedestrians walking
Test Videos: “Abnormal” events only, ex. carts
Perform Data Augmentation to generate “new” video sequences from existing data, using strides
Video Frames from the UCSD Dataset (Courtesy: UCSD)
Non-Anomalous Frame
Anomalous Frame

## Slide 7: Anomaly Detection (Unsupervised)
Convolutional Long Short-Term Memory (LSTM) Autoencoder
Anomaly Classification
Supervised XGBoost (Supervised) vs Simple Linear Threshold

## Slide 8: Unsupervised Learning Model
Convolutional Long Short-Term Memory (LSTM) Autoencoder
Use Unsupervised Machine Learning to reconstruct input images
Combine well-known architectures:
  Convolutional Neural Networks (CNN): To extract Spatial Features from input image
  Convolutional LSTM RNN: To extract Spatial and Temporal Features from input sequences
  Autoencoder: To re-construct input images as best as possible, using only embedded feature maps
Reconstruction Score: A metric that measures the “confidence” of the reconstructed image

## Slide 9: Model Training & Inference ConOps
Training
Inference
Train the Model ONLY on Non-anomalous data
By doing so, we expect the Reconstruction Score (i.e., confidence) to be:
  LOW for Anomalous Data
  HIGH for Non-anomalous Data
Use this metric to Classify the video

## Slide 10: Convolutional Long Short-Term Memory (LSTM) Autoencoder
Individual Pixel Errors
Sum of Errors
Sum of Errors for 10 frames
Normalized Sum of Errors
Reconstruction Cost
Reconstruction Score Calculation

## Slide 11: Anomaly Classification
Reconstruction Score plots reveal no obvious boundary for Anomalous vs Non-anomalous data
Two approaches for Classification of Reconstruction Score vectors:
Simple Linear Threshold:
  Find Threshold Value that provides “optimal” accuracy, despite some mis-classifications
  Able to obtain 70% Accuracy with Threshold at 0.875
Supervised Learning using XGBoost:
  Use Random-Forest Ensemble Tree-based method to “learn” how to Classify the data
  With 90-10 Train-Test split, obtain an accuracy of 50% -> Might as well toss a coin!
  Reason: 70 data-points (34 Train + 36 Test) is insufficient to train an ML model for 190 features

## Slide 12: Results & Conclusion

## Slide 13: Sample Cases
Unsupervised Model performs well
For all anomalous cases, able to determine when anomalous data
Anomalies are indicated by sharp change (drop) in Reconstruction Score
The task of Classification remains difficult
Future Work:
  Improve Unsupervised Model
  Find accurate Classifier
  Transform for Synthetic Space Data
Anomalous Case
Non-Anomalous Case

## Slide 14: Video Anomaly Detection and Classification for Autonomous Deep-Space Robotics
Rohaan Ahmed
Rohaan.Ahmed@Ryerson.ca
Github.com/rohaan-ahmed